## Slide 1
Advanced Irrigation &
Fertigation Technologies
in Horticulture
Precision Water and Nutrient Management for Sustainable Crop Production
Horticulture Technology Series • 2025

## Slide 2
Contents
01
Global Water Challenges in Horticulture
02
Drip & Micro-Irrigation Systems
03
Sprinkler & Sub-Surface Irrigation
04
Fertigation: Principles & Nutrient Delivery
05
Fertigation Equipment & Injection Systems
06
Soil Moisture Sensors & IoT Monitoring
07
Precision Scheduling & Automation
08
Fertigation in Greenhouse Horticulture
09
Water Quality & Treatment Technologies
10
Economic & Environmental Outcomes

## Slide 3
Global Water Challenges in Horticulture
70%
of freshwater used by agriculture
40%
of food grown under irrigation
2×
more efficient — drip vs flood
2050
50% more food needed globally
Key Challenges
Increasing drought frequency and climate variability
Groundwater depletion and rising irrigation costs
Nutrient runoff causing eutrophication of water bodies
Need for higher productivity with reduced resource inputs

## Slide 4
Drip & Micro-Irrigation Systems
How It Works
Water is delivered directly to the root zone via emitters, drippers, or micro-sprinklers at low flow rates (0.5–8 L/hr per emitter). The system operates at low pressure (0.5–2 bar), minimising evaporation and runoff.
System Components
Mainline & submain pipes
Pressure regulators & filters
Drip lines / lateral tubing
Emitters, drippers, misters
Fertigation injectors
30–60%
Water Savings
95%+
Uniform Coverage
Lower leaf wetness
Reduced Disease
Improved yield
Crop Quality
Types of Drip Systems
Surface drip irrigation
Subsurface drip irrigation (SDI)
Tape/T-tape for row crops

## Slide 5
Sprinkler & Sub-Surface Irrigation
Overhead Sprinklers
Simulate rainfall; used for field vegetables, orchards, and nurseries. Types include: fixed risers, rotary heads, and impact sprinklers. Distribution uniformity 75–85%.
Micro-Sprinklers
Low-volume overhead watering (30–200 L/hr). Ideal for orchards and nurseries. Covers 1.5–5 m radius per head. Reduces frost risk.
Subsurface Drip Irrigation (SDI)
Laterals buried 15–45 cm below soil surface
Eliminates surface evaporation losses
No interference with tillage and harvest operations
Water use efficiency up to 95%
Reduces weed germination at surface
System life: 15–20 years with proper management
Selection Criteria: crop type, soil texture, topography, water availability, and capital budget

## Slide 6
Fertigation: Principles & Nutrient Delivery
What is Fertigation?
Fertigation is the application of fertilizers, soil amendments, and other water-soluble products through the irrigation system. It allows precise, timely delivery of nutrients directly to the root zone at the exact growth stage when they are needed.
Macronutrients
Nitrogen (N)
Promotes vegetative growth
Phosphorus (P)
Root development & flowering
Potassium (K)
Fruit quality & disease tolerance
Secondary & Micronutrients
Calcium (Ca)
Cell wall integrity
Magnesium (Mg)
Chlorophyll synthesis
Iron, Zinc, Mn
Enzyme cofactors

## Slide 7
Fertigation Equipment & Injection Systems
Venturi Injector
Uses pressure differential to draw liquid fertilizer into the mainline. Simple, no electricity needed. Accuracy ±10%. Suitable for small farms.
Proportional Pump
Piston or diaphragm pump injects fertilizer proportional to water flow. High precision (±2%). Used in professional horticulture.
Fertigation Controller
Automated EC/pH monitoring with multi-channel dosing. Integrates with sensors and irrigation schedulers. Fully programmable.
Fertilizer Tanks
HDPE or stainless tanks for A+B concentrate stock solutions. Separate tanks prevent precipitation of incompatible nutrients.
Tip: Always inject fertilizer at the downstream side of filtration and upstream of the irrigation zone.

## Slide 8
Soil Moisture Sensors & IoT Monitoring
Sensor Technologies
Tensiometer
Measures soil water tension (kPa); direct measurement of plant-available water
Capacitance (FDR/TDR)
Measures dielectric permittivity; accurate volumetric water content
Neutron Probe
Nuclear moisture measurement; high accuracy but regulated use
Granular Matrix Sensor
Gypsum block type; low cost; electrical resistance method
Infrared/Remote Sensing
Canopy temperature indicates plant water stress; field scale
IoT-Enabled Monitoring
Wireless sensor nodes (LoRa, Zigbee, Wi-Fi)
Real-time data to cloud dashboards
Alerts via SMS/email on threshold breach
Multi-depth sensor arrays
Integration with weather station data
Automated irrigation trigger on soil data
Data logging for crop water use analysis

## Slide 9
Precision Scheduling & Automation
1
Data Collection
Sensors, weather, crop stage
2
ET Calculation
Evapotranspiration (FAO-56)
3
Scheduling Algorithm
Soil water balance model
4
Automated Control
Valve & pump actuation
5
Monitoring & Adjust
Feedback and optimization
Automation Technologies
SCADA Systems
Supervisory control for large irrigation schemes; real-time remote monitoring and control of multiple zones.
Variable Rate Irrigation (VRI)
Zone-by-zone control of sprinkler application rates based on soil variability maps and prescription files.
AI-Based Decision Support
Machine learning models predict crop water demand using historical data, weather forecasts, and satellite imagery.
Weather-Based Controllers
ET-based controllers adjust schedules daily based on local weather station or ET satellite data feeds.

## Slide 10
Fertigation in Greenhouse Horticulture
Soilless / Hydroponic Growing Systems
1
NFT (Nutrient Film Technique)
Thin film of solution flows over roots in channels. Low water use. Common for leafy greens and herbs.
2
Deep Water Culture (DWC)
Roots suspended in aerated nutrient solution. Fast growth. Used for lettuce, basil.
3
Rockwool / Substrate Culture
Inert substrate in slabs or blocks. High-value crops: tomato, pepper, cucumber. EC-controlled fertigation.
4
Aeroponics
Nutrient mist applied to bare roots. Highest oxygenation. Used in vertical farms and research.
EC & pH Management
Target EC 1.5–4.0 mS/cm; pH 5.5–6.5 for optimal nutrient uptake

## Slide 11
Nutrient Solution Management
Chart: Nutrient Demand by Crop Stage
| Seedling | Vegetative | Flowering | Fruit Set | Harvest
N Uptake (relative %) | 15 | 80 | 100 | 85 | 40
K Uptake (relative %) | 10 | 60 | 90 | 100 | 55
Management Practices
Monitor EC and pH daily
Use stock solution A+B separation
Adjust formulation by growth stage
Collect and analyse leachate
Recirculate drainage in closed systems
Flush system periodically to prevent salt buildup
Nutrient Disorders
Deficiencies appear as: chlorosis (Fe, Mg), tip burn (Ca), blossom end rot (Ca in tomato). Toxicities cause leaf scorch and reduced uptake of antagonistic ions. Regular tissue testing prevents both.

## Slide 12
Water Quality & Treatment Technologies
Water Quality Parameters Critical for Irrigation & Fertigation
Parameter
Ideal Range
Risk if Exceeded
pH
6.0–7.0
Emitter clogging, nutrient lock-out
EC (salinity)
< 0.75 dS/m
Osmotic stress, ion toxicity
Hardness (Ca+Mg)
< 200 mg/L
Carbonate precipitation, emitter clogging
Sodium (Na)
< 70 mg/L
Soil structure degradation, leaf burn
Chloride
< 140 mg/L
Toxicity, especially to tree fruits
Iron/Manganese
< 0.5 mg/L
Emitter clogging, filter fouling
Treatment Options: Sand filtration → Disc filters → UV disinfection → Reverse osmosis → Acid/alkali dosing

## Slide 13
Designing a Fertigation Program
01
Soil & Water Analysis
Baseline soil test (N-P-K, pH, EC, organic matter). Source water analysis for existing ions. Identifies what NOT to add.
02
Crop Nutrient Requirements
Consult crop-specific nutrient uptake tables. Account for expected yield target. Split nutrients across growth stages.
03
Calculate Fertilizer Rates
Balance cations/anions in solution. Avoid incompatibilities (Ca+SO4, Ca+PO4). Use software (e.g. Haifa Fertigation App, FertiCalc).
04
Schedule Applications
Link fertigation events to irrigation cycles. Inject in the middle third of irrigation to avoid salt accumulation near emitters.
05
Monitor & Refine
Tissue and soil tests every 2–4 weeks. Adjust concentrations based on growth observations and leachate EC/pH readings.

## Slide 14
Remote Sensing & Precision Agriculture
Integration of remote sensing with irrigation enables zone-specific water and nutrient management, reducing waste and improving uniformity across large horticultural plots.
Satellite Imagery (NDVI)
Normalised Difference Vegetation Index detects crop stress, canopy cover and vigour. Sentinel-2 provides free 10m resolution data every 5 days.
UAV / Drone Mapping
RGB and multispectral cameras map variability at <5 cm resolution. Identifies patchy irrigation coverage, nutrient deficiencies and pest outbreaks.
Thermal Imaging
Canopy temperature mapping identifies water-stressed zones (higher temperature = less transpiration cooling). Triggers site-specific irrigation.
Variable Rate Application
Prescription maps from remote sensing data drive VRI systems and fertigation zones, applying exactly what each area needs.

## Slide 15
Water Use Efficiency & Economic Outcomes
Chart: WUE by Irrigation Method (%)
| Flood | Furrow | Overhead Sprinkler | Micro Sprinkler | Drip | Subsurface Drip
Water Use Efficiency (%) | 40 | 55 | 70 | 80 | 90 | 95
Economic Benefits
↓ 30–50% fertilizer cost with fertigation
↑ 20–40% yield in vegetable crops
↓ 40–60% water costs vs flood
ROI payback: 2–4 years for drip
Reduced labour for application
Lower agri-chemical use
Fertigation increases nutrient use efficiency from ~50% (broadcast) to >90%, delivering major cost savings.

## Slide 16
Environmental Sustainability
Reduced Nutrient Runoff
60%
less N leaching
Precision application means less nitrogen and phosphorus leaching into waterways. Protects aquatic ecosystems from eutrophication.
Lower Carbon Footprint
25%
energy saving
Less pumping energy (lower pressure drip vs sprinklers). Reduced fertilizer manufacture from lower input rates.
Groundwater Conservation
50%
water saved
Efficient irrigation reduces aquifer depletion. Sub-surface drip and soil-moisture-based scheduling are especially effective.
Soil Health Preservation
Better
soil structure
Avoiding waterlogging maintains aerobic soil conditions. Reduced salt accumulation through controlled application.
UN SDG 6 (Clean Water) & SDG 2 (Zero Hunger) — Precision irrigation and fertigation directly advance both goals.

## Slide 17
Case Studies: Real-World Applications
Israel — Avocado Orchards
Subsurface drip + fertigation
40% water saving vs surface; 25% yield increase; fertigation reduced N input by 35% while maintaining fruit quality.
Netherlands — Glasshouse Tomatoes
Rockwool substrate + closed-loop fertigation
Zero discharge system recirculates 100% drain water. EC-controlled dosing achieves 30 kg/m² yield. Water use <15 L/kg fruit.
India — Micro-irrigation (Drip)
Drip irrigation + urea-based fertigation in sugarcane
32% water savings; 15–20% yield increase; fertilizer use efficiency improved from 45% to 78% under fertigation.
Spain — Strawberry Plasticulture
Drip tape under mulch + fertigation
Season-long precise N-P-K delivery; 50% less water than overhead; reduced soil-borne disease; premium early-season yield.

## Slide 18
Challenges & Limitations
High Initial Capital Cost
Drip systems: $800–$4,000/ha. Automated fertigation: $5,000–$50,000. Subsidies and amortisation over crop life needed.
Emitter Clogging
Physical (sediment), chemical (precipitates), and biological (biofilm) clogging. Requires filtration, flushing, and acid dosing.
Technical Knowledge Gap
Farmers need training on EC/pH management, nutrient solution formulation, system maintenance, and sensor interpretation.
Water Source Limitations
High salinity or bicarbonate water reduces efficiency. Pre-treatment (RO, acidification) adds cost and complexity.
Soil Variability Challenges
Heterogeneous soils cause non-uniform water distribution. Requires detailed site characterisation and zone mapping.
System Maintenance
Filters, emitters, injection pumps, and sensors all need regular servicing. Neglect leads to rapid performance decline.

## Slide 19
Future Trends in Irrigation & Fertigation
Now–2027
AI Crop Models
Deep learning models predict crop water demand with >90% accuracy using real-time satellite + sensor fusion.
2025–2028
Nano-Fertigation
Nano-encapsulated nutrients with controlled-release coatings applied via irrigation for ultra-precise delivery.
2026–2030
Digital Twins
Virtual farm replicas simulate water-nutrient dynamics, enabling predictive management and scenario planning.
2027–2032
Autonomous Robots
Mobile irrigation robots with on-board sensors and drippers apply water crop-by-crop in protected horticulture.
2025–2030
Biostimulant Fertigation
Seaweed extracts, humic acids, and microbial inoculants delivered via fertigation to enhance nutrient uptake.
2028+
Circular Water Systems
Constructed wetlands + treated wastewater + biochar filtration create closed loops for nutrient and water recovery.

## Slide 20
Key Takeaways
Drip and micro-irrigation are the most water-efficient systems, achieving 90–95% WUE
Fertigation improves nutrient use efficiency from ~50% to >90%, cutting fertilizer costs by 30–50%
IoT sensors, automation, and AI scheduling are transforming irrigation from reactive to predictive management
Greenhouse fertigation with closed-loop nutrient solutions achieves near-zero waste and maximum yield
Precision irrigation directly advances food security and environmental sustainability goals (SDG 2, 6)
The future lies in integrated digital platforms combining sensors, AI, remote sensing, and robotics
"Grow more with less — precision water and nutrient management is the cornerstone of sustainable horticulture."